## Slide 1: Mitigation of the Spectrum Sensing Data Falsifying Attack in Cognitive Radio Networks
Rajorshi Biswas, Jie Wu, and Xiaojiang Du
Dept. of Computer and Information Sciences
Temple University

## Slide 2: Road Map
  Cooperative spectrum sensing
  Previous work
  Majority voting and existing models
  Weighted majority voting with confidence
  Simulation results
  Extension: two-level majority voting
  Conclusion

## Slide 3: 1. Cooperative Spectrum Sensing
  Primary user (PU)
    Licensed user, high priority
  Secondary user (SU)
    Send sensing information to aggregator
  Malicious secondary user (MSU)
    Send opposite sensing information to aggregator
  Aggregator
    Does majority voting
    Results are sent back to SUs and MSUs
SU
Aggregator
PU=1
0
1
1
1
1
1
MSU
PU=1
1
1
1
0
0
0
SU’s wrong sensing and MSU’s result
can change aggregator’s decision
Solution: reduce weight of MSUs through reputation
Notes: PU=1: primary user present
PU=0: primary user absent
First figure:
SU can make mistake.
Second figure:
MSU sends opposite sensing information. MSU can also make mistake. MSUs mistake provides current result to aggregator.
SU/MSU ranges
S. Maric, S. Reisenfeld and L. Goratti, "A simple and highly effective SSDF attacks mitigation method," 2016 10th International Conference on Signal Processing and Communication Systems (ICSPCS), Gold Coast, QLD, 2016
Number of SU: 35
Number of MSU: 15
(From another paper)
MSU+SU=20
% of MSU varied 0%-95%

## Slide 4: 2. Previous Work
MSU detection systems | Limitations
Linear reputation-based system. SUs send raw sensing information to Aggregator. If a SU agrees with aggregator, reputation increases by “1” or decreases by “1”. | Computation overhead is high for processing raw sensing information. Linear reputation update mechanisms are not efficient enough.
Active transmission-based system. | PU emulated signals can be detected. MSU will respond correctly to emulated signal.
R. Chen, J. -. Park and K. Bian, "Robust Distributed Spectrum Sensing in Cognitive Radio Networks," IEEE INFOCOM 2008.
T. Bansal, B. Chen, and P. Sinha, “Fastprobe: Malicious user detection in cognitive radio networks through active transmissions,” in IEEE INFOCOM 2014.
PU emulated signal
Sensing result
Notes: Why computation overhead is high?
Aggregator need to process raw sensing information.

## Slide 5: 3. Majority Voting and Existing Models
If > 0.5
Aggregator’s decision=1
Else
Aggregator’s decision=0
Update reputation of SUs and MSUs using Reputation Update Function (RUF)
Aggregator makes decision
Initial reputation=1
normalized reputation
Notes: Range of =[0,1]
Lecture note 16. paper will be provided.
Range of =[0,1]
This factor can be varied according to system requirements. This is a simplified method of recording reputation, and more complicated representations, such as a Beta distribution may yield better performance. From paper DRBTS: Distributed Reputation-based Beacon Trust System (jie wu, avinash)
Range of 𝜼 =[0,1]
Lecture note 16. paper will be provided.
Range of 𝝁 =[0,1]
This factor can be varied according to system requirements. This is a simplified method of recording reputation, and more complicated representations, such as a Beta distribution may yield better performance. From paper DRBTS: Distributed Reputation-based Beacon Trust System (jie wu, avinash)

## Slide 6: Majority Voting and Existing Models
Linear RUF:
= priority of previous reputation
Multiplicative RUF: *
= learning rate: [0, 1]
Multiplicative RUF with sliding window:
  If SU’s result = aggregator’s result
  Else
  (or 0, no decrease)
-1 | 1 | 1 | 1 | -1 | 1 | 1
Sliding window
*Arora, Sanjeev, Elad Hazan, and Satyen Kale. "The multiplicative weights update method: a meta-algorithm and applications." Theory of Computing 8.1 (2012)
Notes: Range of =[0,1]
Lecture note 16. paper will be provided.
Range of =[0,1]
This factor can be varied according to system requirements. This is a simplified method of recording reputation, and more complicated representations, such as a Beta distribution may yield better performance. From paper DRBTS: Distributed Reputation-based Beacon Trust System (jie wu, avinash)
Range of 𝜼 =[0,1]
Lecture note 16. paper will be provided.
Range of 𝝁 =[0,1]
This factor can be varied according to system requirements. This is a simplified method of recording reputation, and more complicated representations, such as a Beta distribution may yield better performance. From paper DRBTS: Distributed Reputation-based Beacon Trust System (jie wu, avinash)

## Slide 7: 4. Weighted Majority Voting with Confidence
  = Normalized confidence
Minority: 30
Majority: 70
confidence
Adaptive Multiplicative RUF
Without confidence
SU1 | 1 | 2.71 | 7.38 | 20.08 | 54.59
SU2 | 1 | 2.71 | 1 | 2.71 | 7.38
SU3 | 1 | 2.71 | 7.38 | 20.08 | 54.55
MSU1 | 1 | 2.71 | 7.38 | 2.71 | 1
MSU2 | 1 | 0.36 | 0.13 | 0.36 | 0.13
A | 1 | 1 | 0 | 1 | 0
Time | 0 | 100 | 200 | 300 | 400
PU | 1 | 0 | 0 | 1 | 1
SU1 | 1 | 1 | 0 | 1 | 1
SU2 | 1 | 0 | 0 | 1 | 1
SU3 | 1 | 1 | 0 | 1 | 0
MSU1 | 1 | 1 | 1 | 0 | 0
MSU2 | 0 | 0 | 0 | 0 | 0
A | 1 | 1 | 0 | 1 | 0
 | 0.6 | 0.2 | 0.6 | 0.2 | 0.2
SU1 | 1 | 1.82 | 2.22 | 4.05 | 4.95
SU2 | 1 | 1.82 | 1.49 | 2.71 | 3.32
SU3 | 1 | 1.82 | 2.22 | 4.05 | 4.95
MSU1 | 1 | 1.82 | 2.22 | 1.22 | 1
MSU2 | 1 | 0.54 | 0.44 | 0.81 | 0.67
A | 1 | 1 | 0 | 1 | 1
 | 0.6 | 0.2 | 0.6 | 0.2 | 0.2
SU1 | 1 | 1.82 | 2.22 | 4.05 | 4.95
SU2 | 1 | 1.82 | 1.49 | 2.71 | 3.32
SU3 | 1 | 1.82 | 2.22 | 4.05 | 4.95
MSU1 | 1 | 1.82 | 2.22 | 1.22 | 1
MSU2 | 1 | 0.54 | 0.44 | 0.81 | 0.67
A | 1 | 1 | 0 | 1 | 1
With confidence
Majority voting
High variance
Low variance
reputation
reputation
Ground truth
Sensing
result
False positive
False negative

## Slide 8: 5. Simulation
  Settings and datasets
  Number of SUs: 10-50
  SU error rate: 0-0.3 (randomly selected)
  Number of MSUs: 7-50
  MSU error rate: 0.7-1 (randomly selected)
  Initial reputation: 1
  Sensing records of 100,000 timeslots.
SU
MSU
time
SU
MSU
time
MSU
Dataset type 1
Dataset type 2
MSUs build reputation
Attack

## Slide 9: Multiplicative vs. Adaptive Multiplicative RUF
SU/MSU: 50/40
SU/MSU: 50/40
SU/MSU: 50/50
SU/MSU: 50/50
Dataset type 1 Used for simulation.
False positive (FP), False negative (FN), Error (ER), Adaptive multiplicative (ADA MULT), Multiplicative (MULT)
Notes: Higher value of : quick convergence.
Higher number of MSU: higher error rate.
Higher value of 𝜂 : quick convergence.
Higher number of MSU: higher error rate.

## Slide 10: Multiplicative vs. Adaptive Multiplicative RUF
High variation of reputation in multiplicative RUF leads to more errors.
Dataset type 2 with
Multiplicative
Adaptive multiplicative
Notes: Multiplicative & adaptive multiplicative is in different scale.
Multiplicative: High variance in SUs’ reputation leads to higher number of error. Mistake from highly reputed SU leads aggregator to make mistake.
Adaptive-multiplicative: SUs reputation are similar.

## Slide 11: 6. Extension: Two-Level Majority Voting
  13 MSUs (clustered)
  13 SUs
  2 wrong aggregators
  4 correct aggregators.
Connected dominating set based distributed aggregator selection process
  MSUs may win in one-level voting
  MSU cannot win in two-level voting

## Slide 12: Two-Level vs. One-Level Voting
Two-level voting works better when MSUs are clustered
Dataset type 2 with
SU/MSU: 50/40
MSUs are sparse (uniform).
MSUs are clustered.
False positive (FP), False negative (FN), Error (ER), Level 1 (LVL 1), and Level 2 (LVL 2)
80% MSU: clustered
20% MSU and all SU: uniformly distributed

## Slide 13: 7. Summary
  Adaptive multiplicative RUF using confidence
  Adaptive multiplicative RUF works better than other RUFs
  Two-level voting produces less errors than one-level voting
SU
Aggregator
PU=1
0
1
1
1
1
1